## Slide 1: Circuit Construction Kit Clicker questions
Three activities by Trish Loeblein
phet.colorado.edu
Introduction to Electrical circuits
Resistors in Series and Parallel Circuits
Combo Circuit Lab

## Slide 2: Introduction to Electrical circuits
Learning Goals: Students will be able to
Discuss basic electricity relationships
Analyze the differences between real circuits and the simulated ones
Build circuits from schematic drawings
Use a multimeter to take readings in circuits.
Provide reasoning to explain the measurements and relationships in circuits.

## Slide 3: 1.If you build this circuit with real equipment, how would you determine the resistance of the resistor?
Use the ohmmeter after connecting the battery.
Use the ohmmeter before connecting the battery.
Measure the current and voltage, then use Ohm’s law
Two of the above.
Notes: C. You cannot use the ohm meter when there is power to the resistor and measuring the resistance without power will give a value that is less than when powered.

## Slide 4: 2.If you increase the voltage of the battery, how will the light bulb change?
It will be look brighter because the yellow lines are brighter and longer
It will be less bright because the yellow lines are less bright and shorter
There is no change because the bulb just uses the extra energy without changing brightness
Notes: A More voltage means more energy so it will be brighter

## Slide 5: 3.If you increase the voltage of the battery, how will the electron display change?
The blue dots will get bigger to show more energy is being used
The blue dots will move faster to show more energy is being used
There is no change
Notes: B you could just say V=IR and since no change in resistance current goes up, but you might want to discuss why the electron size isn’t used to indicate more energy.

## Slide 6: 4. If you build circuit A and then add a resistor as in circuit B, the light will
Look brighter
Look less bright
There will no change in brightness
A
B
Notes: B more resistance means less current to bulb.

## Slide 7: Resistors in Series and Parallel Circuits
Learning Goals: Students will be able to
Discuss basic electricity relationships in series and parallel circuits
Analyze the differences between real circuits and the simulated ones
Build circuits from schematic drawings
Use a multimeter to take readings in circuits.
Provide reasoning to explain the measurements in circuits.

## Slide 8: 1. Which shows the correct way to use an ammeter?
A B
Notes: B

## Slide 9: 2. Which resistor will have the greatest current?
50 
10 
They have the same current
Notes: B

## Slide 10: 3. Which resistor will have the greatest current?
The top resistor
The lower resistor
They have the same current
Notes: C

## Slide 11: 4. Which resistor will have the greatest voltage?
The top resistor
The lower resistor
They have the same voltage
Notes: c

## Slide 12: 5. Which resistor will have the greatest voltage?
50 
10 
They have the same voltage
Notes: C

## Slide 13: 6. Which resistor will have the greatest voltage?
50 
10 
They have the same voltage
Notes: A

## Slide 14: 7. Which resistor will have the greatest current?
50 
10 
They have the same current
Notes: C

## Slide 15: 8. Which resistor will have the greatest voltage?
The top resistor
The lower resistor
They have the same voltage
Notes: C

## Slide 16: 9. Which resistor will have the greatest current?
The top resistor
The lower resistor
They have the same current
Notes: C

## Slide 17: 10. What will happen if the voltage of the battery is increased to 25 volts?
The voltage across the resistor will increase
The voltage across the resistor will decrease
The voltage of the resistor does not change
Notes: A

## Slide 18: 11. What will happen if the voltage of the battery is increased to 25 volts?
The current through the resistor will increase
The current through the resistor will decrease
The current of the resistor does not change
Notes: A

## Slide 19: Combo Circuit Lab
Learning Goals: Students will be able to:
Analyze the differences between real circuits and the ideal ones,
Build circuits from schematic drawings,
Use a multimeter to take readings in circuits.
Provide reasoning to explain the measurements in circuits.

## Slide 20: 12. What is the total resistance in this circuit?
6.4 
21 
38 
75 
Notes: B [1/(30+40) + 1/45]^-1 =21

## Slide 21: 13. What is the total resistance in this circuit?
6.4 
21 
38 
75 
Notes: C. [1/(45+10) ]^-1 + 30=38